Traffic modeling  /  Helsinki CCZ case

We implement traffic modeling by employing the expertise of the Transport department of the Helsinki Metropolitan Area Council (HMAC). The HMAC uses an EMME/2 traffic planning system tailored for routine long-term traffic planning in the HMA (Elolähde, 2006), with predictions currently running upto year 2030. The system utilizes logit models, producing hourly traffic volumes (by vehicle type) and speeds for ~3200 unidirectional links representing the major roads and streets of the HMA. A tailored model for congestion charging scenarios has been previously developed. We will utilize this model with some modifications, feeding in contextual data (e.g. housing, jobs, costs) from year 2005.

A simplified description of the traffic model is given below (extracted from Elolähde (2006)).

1.  General aspects and key concepts

The full model consists of four sub-models: 1) trip generation 2) destination choice 3) mode choice and 4) route choice. Trips are divided into four categories: home-based (work, school, other) and non-home-based. For passenger transport, there are three (or five) modes: cars, public transit (subdivided into bus/tram and metro/train), and light traffic (subd. into walking and cycling). Freight transport is subdivided into trucks and vans.

Input data for the models includes e.g. the number of inhabitants, jobs and cars in each zone, as well as the number of transfers, modal travel times, and costs between each pair of zones.

2.  Description of traffic submodels

Trip generation models are based on average trip production rates. As its output, the model produces the number of trips originating from each zone, by trip category.

Destination choice and mode choice models are logit models (see below), except for school trips. Their output consists of demand matrices for each mode (i.e. the number of trips between each pair of zones).

Route choice models describe the distribution of traffic within a network. The network for non-public transport vehicles (mostly personal cars) consists of road links (characterized by e.g. length, number of lanes, and volume-delay function), and nodes (i.e. intersections). In HMAC model, the network has 129 zones and 1600 bidirectional links. A demand matrix is assigned on the network, producing volumes and speeds for each link. The assignment method is a capacity restrained equilibrium. Part of an example result matrix is shown below:

The network for public transport consists of lines, characterized by a route (a chain of nodes) and average headway, a transit network, and connectors (walking links between zones and bus stops). The HMA transit network consists of 4 800 bus links, 300 tram links, and 100 heavy rail links. Assignment of the public transport demand matrix on the network produces travel times and the number of transfers between zones.

3.  Logit models

Destination and mode choice models are logit models, in which the probability Pi of choosing alternative "i" is given by

where Vi is the benefit function of alternative i:    Vi = β1 x1i + β2 x2i +  ... +  βn xni   in which βk is the coefficient of variable k, and xik is the value of variable xi in alternative k. The coefficients βk  have been estimated when constructing the model. The variables and coefficients used in HMAC-Transport models are listed in the table below.

| Model | Variables | coefficients (β) |
| --- | --- | --- |
|  |  | home-based work trips | other home- based trips | non-home- based trips |
| destination | scale factor | ms107 | ms157 | ms207 |
| destination | ln(jobs) | ms108 | ms158 | ms208 |
| destination | dummy of the zone | ms109 | ms159 | ms209 |
| mode | dummy, walk | ms110 | ms160 | ms210 |
| mode | dummy, bus+tram | ms111 | ms161 | ms211 |
| mode | dummy, car | ms112 | ms162 | ms212 |
| mode | dummy, bicycle | ms113 | ms163 | ms213 |
| mode | dummy, heavy rail | ms114 | ms164 | ms214 |
| mode | travel cost, heavy rail | ms115 | ms165 | ms215 |
| mode | travel cost, bus+tram | ms116 | ms166 | ms216 |
| mode | travel cost, car | ms117 | ms167 | ms217 |
| mode | parking ratio | ms118 | ms168 | ms218 |
| mode | parking cost | ms119 | ms169 | ms219 |
| mode | nr of transfers, bus+tram | ms120 | ms170 | ms220 |
| mode | travel time, bus+tram | ms121 | ms171 | ms221 |
| mode | travel time, car | ms122 | ms172 | ms222 |
| mode | # of transfers, heavy rail | ms123 | ms173 | ms223 |
| mode | travel time, heavy rail | ms124 | ms174 | ms224 |
| mode | ln(distance), walk | ms125 | ms175 | ms225 |
| mode | distance 0-5 km, walk | ms126 | ms176 | ms226 |
| mode | distance 5-10 km, walk | ms127 | ms177 | ms227 |
| mode | ln(distance), bicycle | ms130 | ms180 | ms230 |
| mode | distance 0-5 km, bicycle | ms131 | ms181 | ms231 |
| mode | distance 5-10 km, bicycle | ms132 | ms182 | ms232 |
| mode | cars/household | ms135 | ms185 | ms235 |
| mode | share of cars provided by employer | ms136 | ms186 | ms236 |
| mode | image of bus traffic | ms138 | ms188 | ms238 |
| mode | image of heavy rail traffic | ms139 | ms189 | ms239 |
| mode | logsum walk+bicycle | ms141 | ms191 | ms241 |
| mode | logsum transit | ms142 | ms192 | ms242 |
| mode | number of modes | ms149 | ms199 | ms249 |

4.  Other considerations

Additional steps and complications in traffic modeling include the treatment of external trips (traffic from beyond the HMA), trips to/from the airport (handled by separate models), and the treatment of freight transport (trucks, vans). For the prediction of congestion charging scenarios, further complications relate to the treatment of fees that vary by area and time of day. In the traffic model, congestion fees are added on top of other travel costs and affect both mode and route choices.

5.  Overall model

The simplified flowchart below illustrates the main steps of traffic modeling (omitting e.g. light traffic), and the role of congestion fees therein.

6.  Validity of the model predictions

The traffic models used by HMA Council have been estimated in the Laboratory of Transportation Engineering of the Helsinki University of Technology, based on revealed-preferences data from autumn 2000 travel survey, including information about weekday trips made by ~8 700  inhabitants of the HMA. The total number of trips was ~28 000. Over 50 model sets have been estimated and tested, varying the set of variables, parameters, and submodel hierarchy. Supporting the validity of the results, the traffic model is routinely used for long-term traffic planning in the HMA.

When the Helsinki CCZ predictions are viewed in light of the fee levels (Table 2) and zone dimensions, the results show a good agreement with empirical data from existing CC areas. In Stockholm, a 2.2 € peaktime cost per passage resulted in a 16–24 % acute decline in daily passages (Höök, 2007), while in London, a ~7.5€ (in 2003) daily charge resulted in reductions of 18% in (4-wheel-vehicles and 30% in potentially-chargeable vehicles entering the central London zone during the charging times (07-18) (TfL, 2007). The predictions are also in line with results obtained using Dublin Transportation office's model (Rogers and Eagney, 2008) as well as with models utilizing transport demand elasticities (Oum et al., 1992; Roth and Villoria Jr, 2001).

References

Elolähde, T., 2006. Traffic Model System and Emission Calculations of the Helsinki Metropolitan Area Council, 20th International Emme Users' Conference.

Höök, B., 2007. Trängselskatt - dag 1. Pressträff Trafik Stockholm Stockholm Vägverket. http://www.vv.se/filer/46588/VV_%20presskonf_070802.pdf.

Oum, T. H., Waters, W. G. and Yong, J. S., 1992. Concepts of Price Elasticities of Transport Demand and Recent Empirical Estimates - an Interpretative Survey. Journal of Transport Economics and Policy 26, 139-154.

Rogers, M. and Eagney, C., 2008. Congestion charging in Dublin. Proceedings of the Institution of Civil Engineers-Transport 161, 143-147.

Roth, Gabriel and Villoria Jr, Olegario, 2001. Finances of Commercialized Urban Road Network Subject to Congestion Pricing. Transportation Research Record: Journal of the Transportation Research Board 1747, 29-35.

TfL, 2007. Central London Congestion Charging. Impacts Monitoring. Fifth Annual Report. Transport for London. http://www.tfl.gov.uk/assets/downloads/fifth-annual-impacts-monitoring-report-2007-07-07.pdf.